## Slide 1: Robotic Arm with enhanced reachable workspace
Rigved kulkarni & alec lahr

## Slide 2: Agenda
Problem & Motivation
Method
Robot Design
Forward Kinematics
Inverse Kinematics
Simulation
Challenges
Individual Contributions
Conclusion

## Slide 3: Problem & Motivation
Original project topic: Comau NM45 robot arm
Noticed limited reachable workspace problem
Revised project topic: Design a robot arm with a fuller
reachable workspace

## Slide 4: Method
Identify constraints on workspace
Sketch concept design
Create CAD model
Simulate robot
Link 2 geometry

## Slide 5: Robot Design
C-Shaped link 2 Spherical wrist

## Slide 6: Forward Kinematics
 | α | a | d | Θ
0-1 | -90 | 0 | 0 | Θ1
1-2 | 0 | 0 | 0 | Θ2-90
2-3 | 0 | a3 | 0 | 0
3-d | -90 | ad | 0 | Θ3
d-4 | 0 | 0 | d4 | 0
4-5 | 90 | 0 | 0 | Θ4
5-6 | -90 | 0 | 0 | Θ5
6-7 | 0 | 0 | d7 | Θ6

## Slide 7: Inverse Kinematics
Position
Θ1 = atan2(OX-d7r13, OY-d7r23)
Θ3 = ±(atan(d4/ad)+acos(-((OX-d7r13)2+(OY-d7r23)2+(OZ–d7r33)2- a32 - a42) / (2a3a4))-π)
Θ2 = atan2((OX-d7r13)2+(OY-d7r23)2, OZ-d7r33)±atan(a4sinΘ3*/(a3+a4cosΘ3*))
Rotation
Θ4 = atan2(r13, r23)
Θ5 = atan(sqrt(1 - r332) / r33)
Θ6 = atan2(-r31, r32)
Spherical wrist enables
IK separability!

## Slide 8: Simulation – Arm reachability
theta1:0, theta2:0, theta3:0, theta4:0,theta5:0, theta6:0
theta1:pi/2, theta2:-pi/2, theta3:0, theta4:pi,theta5:0, theta6:0

## Slide 9: Simulation – motion planning

## Slide 10: Challenges
Choosing robot dimensions to avoid self-collision while minimizing weight
Robot toppling due to small base and higher position of center of mass. Countered by increasing the surface area of the base
Unclean reexport to URDF messed up joint origins

## Slide 11: Conclusion
Spherically Reaching Robotic Arm benefits:
  Increased reachable workspace
  Increase in number of configurations for the same end position
Path planning library benefits:
  Smoother transition between configurations
  Collision free optimal path generation

## Slide 12: Individual Contributions
B O T H
Problem formulation
Robot design
A L E C
CAD model
Forward kinematics
Inverse kinematics
R I G V E D
Gazebo & RViz visualization
Path planning algorithm

## Slide 13: References
Statista. (2020). Size of the global industrial automation market from 2019 to 2026. https://www.statista.com/statistics/1219772/industrial-automation-market-size-worldwide/
Mark W. Spong, Seth Hutchinson, and M. Vidyasagar John Wiley & Sons (2006), Robot Modeling and Control, ISBN-10 0-471-64990-2
http://wiki.ros.org/
https://answers.gazebosim.org/
https://answers.ros.org/